## Slide 1: Sensor Subsystem Design
Aniruddh Pandey

## Slide 2: Sensor Subsystem Overview
Presenter: Name goes here
Sensor Type | Model | Purpose | Location
Pressure | BMP280 | To calculate altitude using the air pressure | Carrier
GPS | NEO-M8N | To track the position of the carrier | Carrier
IMU | MPU9250 | To detect the carrier’s orientation and the direction in which it’s heading | Carrier
Temperature | BMP280 | To read the air temperature | Payload
Pressure | BMP280 | To calculate altitude using the air pressure | Payload
Air Speed | MPXV7002DP | To detect the air speed | Payload

## Slide 3: Payload Air Pressure Sensor Trade & Selection
Presenter: Name goes here
Model | Interface | Current Draw @1Hz | Supply Voltage | Resolution (hPa) | Accuracy (hPa) | Temperature range (°C) | Size (mm) | Cost ($)
MS5611 | I2C & SPI | 1.5 mA | 5 V | 0.012 | ±1.5 | -40 to 85 | 18x14 | 12.23
BMP280 | I2C & SPI | 1.12 mA | 3.3 V | 0.01 | ±1 | -40 to 85 | 15x12 | 0.88
MPL311A52 | I2C | 2 mA | 3.3 V | 0.015 | ±4 | -40 to 85 | 18x19 | 14.95
Selected : BMP280
Rationale : highest accuracy and resolution, less size and low cost

## Slide 4: Payload Air Temperature Sensor Trade & Selection
Presenter: Name goes here
Model | Interface | Current Draw @1Hz | Supply Voltage | Resolution (°C) | Temperature range (°C) | Size (mm) | Cost ($)
MS5611 | I2C & SPI | 1.5 mA | 5 V | 0.01 | -40 to 85 | 18x14 | 12.23
BMP280 | I2C & SPI | 1.12 mA | 3.3 V | 0.01 | -40 to 85 | 15x12 | 0.88
Selected : BMP280
Rationale : Already being used as pressure sensor
Has good resolution and sufficient range

## Slide 5: Payload Air Speed Trade & Selection
Presenter: Name goes here
Model | Interface | Current Draw | Measurement Range | Resolution | Cost ($)
MPXV7002DP | Analog | 10 mA | 1 psi, 100 m/s | 0.84 Pa | 26.96
MS4525DO | I2C & SPI | 3 mA | 1 psi, 100 m/s | 0.84 Pa | 52.91
Selected : MPXV7002DP
Rationale : Easy to program
Is reliable and almost half the cost of the
other option

## Slide 6: Container Air Pressure Sensor Trade & Selection
Presenter: Name goes here
Model | Interface | Current Draw @1Hz | Supply Voltage | Resolution (hPa) | Accuracy (hPa) | Temperature range (°C) | Size (mm) | Cost ($)
MS5611 | I2C & SPI | 1.5 mA | 5 V | 0.012 | ±1.5 | -40 to 85 | 18x14 | 12.23
BMP280 | I2C & SPI | 1.12 mA +3.93 of mpu9250 | 3.3 V | 0.01 | ±1 | -40 to 85 | 15x12 | 10.88
MPL311A52 | I2C | 2 mA | 3.3 V | 0.015 | ±4 | -40 to 85 | 18x19 | 14.95
Selected : BMP280
Rationale : highest accuracy and resolution, and the sensor is available with the IMU module on the same PCB

## Slide 7: Container GPS Sensor Trade & Selection
Presenter: Name goes here
Model | Interface | Supply Voltage | Current Draw | Resolution (m) | Cold Start time (s) | Size (mm) | Weight (g) | Cost ($)
Neo-6M | SPI / I2C/ UART / USB | 3.3 V | 37 mA | 2.5 | 27 | 22x30x4 | 12 | 9.5
Neo-M8N | SPI / I2C/ UART / USB | 3.3 V | 23 mA | 2-2.5 | 30 | 26x36x4 | 17 | 18.88
Adafruit ultimate gps | UART & I2C | 3.3/5 V | 20 mA | 1.8 | 34 | 15x15x4 | 8.5 | 40
Selected : NEO-M8N
Rationale : Supports 72 receiving channels and is reliable

## Slide 8: Container Orientation Sensor Trade & Selection
Presenter: Name goes here
Model | Interface | Accelerometer range(g) | Gyroscopic range(°/s) | Magnetometer range(μT) | Current Draw | Cost ($)
MPU9250 | I2C & SPI | ±2g, ±4g, ±8g, ±16 g | ±250°/s, ±500°/s, ±1000°/s, ±2000°/s | ±4800μT | 3.93 mA (+1.12 of BMP280) | 10.88
BMX055 | I2C & SPI | ±2g, ±4g, ±8g, ±16 g | ±125°/s, ±250°/s, ±500°/s, ±1000°/s, ±2000°/s | ±1300μT (x,y), ±2500μT (z) | 5.63 mA | 
Selected : MPU9250
Rationale : Easily available and programable
High reliability and the module also has
BMP280 pressure sensor

## Slide 9: Communication and Data Handling (CDH) Subsystem Design
Aniruddh Pandey

## Slide 10: Container Command Data Handler (CDH) Overview
Presenter: Name goes here
NEO-M8N
It is going to act as the RTC module
Arduino Nano
Microcontroller
Data collector and processor
XBee Pro S2C
Transmit and receive data

## Slide 11: Container Processor & Memory Trade & Selection
Presenter: Name goes here
Selected : Arduino nano
Rationale : Sufficient number of pins
Low cost
Easy to program
Microcontroller | Processor Speed (MHz) | Boot time | Interfaces | RAM (kB) | Operating Voltage | Weight (g) | Cost ($)
Arduino Nano | 16 | 8-10 | 1 SPI,1 I2C, 1 UART | 2 | 5 V | 7 | 4.75
Teensy 3.6 | 180 | 15 | 3 SPI, 3 I2C, 7UART | 256 | 3.3 V | 4.9 | 29.25
Teensy 4.0 | 600 | 5 | 3 SPI,4 I2C, 6 UART | 1024 | 3.3 V | 10 | 19.95

## Slide 12: Container Real-Time Clock
Presenter: Name goes here
Model | Operating Voltage (V) | Current (mA) | Accuracy (ppm) | Hardware/ Software | Cost ($)
Arduino nano | 5 | 19 | 50 | Software | Free( comes with Arduino )
NEO-M8N | 3.3 | 23 | 20 | Hardware | Free( comes with the GPS )
Selected : NEO-M8N
Rationale : It has backup battery to maintain mission
time in case of system reset due to power
interuption
High accuracy

## Slide 13: Container Radio Configuration
Presenter: Name goes here
Model | Operating frequency (GHz) | Transmitting power(dBm) | Receiver sensitivity(dBm) | Transmit current (mA) | Range (km)
XBee-Pro S2C | 2.4 | +18 | -101 | 120 | 3.2
XBee-Pro S2C is selected for radio communication
The container will have only 1 XBee
Configuration the XBee will be done using XCTU software
This XBee will have the coordinator role
Data transmission will be done in broadcast mode

## Slide 14: Container Telemetry Format 1 of 2
Presenter: Name goes here
Data Format | Example | Description
Mission time | 12:15:45 | is UTC time in format hh:mm:ss, where hh is hours, mm is minutes, and ss is seconds
Packet count | 245 | the count of transmitted packets which is to be maintained through processor reset
Packet type | C | the character ‘C’ for carrier telemetry and ‘SP’ for science payload
Altitude | 500 | the altitude in meters relative to ground level. Resolution is <0.1m
Latitude | 4124.2028 | is the latitude generated by the GPS receiver in decimal degrees with a resolution of 0.0001 degrees
Longitude | 210.4418 | is the longitude generated by the GPS receiver in decimal degrees with a resolution of 0.0001 degrees.
Pitch | 64 | is the tilt angle in the pitch axis in degrees
Roll | 72 | is the tilt angle of the roll axis in degrees
Yaw | 60 | is the tilt angle of the yaw axis in degrees

## Slide 15: Container Telemetry Format 2 of 2
Presenter: Name goes here
Data packet will be transmitted at the rate of 1 Hz in burst
Carrier data packet format :
<Mission_Time>, <Packet_Count>, <Packet_Type>, <Altitude>, <Latitude>,<Longitude>,<Pitch>,<Roll>,<Yaw>
Science payload data relayed by carrier data packet format:
<Packet_Count>,<Packet_Type>,<Altitude>,<Temperature>,<Air_Speed>
Data packet will be stored in a CSV file named “Carrier.csv”
Data packet will be stored in a CSV file named “Science_payload.csv”
Example:
12:15:45,245,C,500,4124.2028,210.4418,64,72,60
Example:
23,SP,500,20,20

## Slide 16: Payload CDH Overview
Presenter: Name goes here
Arduino Nano
Microcontroller
Data collector and processor
XBee Pro S2C
Transmit and receive data

## Slide 17: Payload Processor & Memory Trade & Selection
Presenter: Name goes here
Microcontroller | Processor Speed (MHz) | Boot time | Interfaces | RAM (kB) | Operating Voltage | Weight (g) | Cost ($)
Arduino Nano | 16 | 8-10 | 1 SPI,1 I2C, 1 UART | 2 | 5 V | 7 | 4.75
Teensy 3.6 | 180 | 15 | 3 SPI, 3 I2C, 7UART | 256 | 3.3 V | 4.9 | 29.25
Teensy 4.0 | 600 | 5 | 3 SPI,4 I2C, 6 UART | 1024 | 3.3 V | 10 | 19.95
Selected : Arduino nano
Rationale : Sufficient number of pins
Low cost
Easy to program

## Slide 18: Payload Radio Configuration
Presenter: Name goes here
Model | Operating frequency (GHz) | Transmitting power(dBm) | Receiver sensitivity(dBm) | Transmit current (mA) | Range (km)
XBee-Pro S2C | 2.4 | +18 | -101 | 120 | 3.2
XBee-Pro S2C is selected for radio communication
The payload will have only 1 XBee
Configuration the XBee will be done using XCTU software
This XBee will be configured as an end device
Data transmission will be done in unicast mode

## Slide 19: Payload Telemetry Format
Presenter: Name goes here
Data Format | Example | Description
Packet count | 25 | the count of transmitted packets which is to be maintained through processor reset
Packet type | SP | the character ‘C’ for carrier telemetry and ‘SP’ for science payload
Altitude | 500 | the altitude in meters relative to ground level. Resolution is <0.1m
Temperature | 20 | is the measured temperature in degrees Celsius with a resolution of 0.1
Air Speed | 20 | the air speed relative to the payload in meters/second
Data Format :
<Packet_Count>,<Packet_Type>,<Altitude>,<Temperature>,<Air_Speed>
Example:
23,SP,500,20,20
Data packet will be stored in a CSV file named “Science_payload.csv”
Data packet will be transmitted from payload to container and relayed to GCS at 1Hz in burst

## Slide 20: Electrical Power Subsystem (EPS) Design
Aniruddh Pandey

## Slide 21: EPS Overview (1 of 4)
Presenter: Name goes here
Component | Purpose
3.6V ½AA Lithium Battery | Power source for the electronic system in payload as well as the container
NCR18650B Li-Ion Battery | Power source for the brushless drone motor
Switch | To connect and disconnect the battery from the circuit
Microcontroller | To provide 3.3V and 5V power bus to the sensors
3.3V regulator | To provide 3.3V power bus to the XBee radio module
Sensors | To provide environment measurements to the Arduino
XBee | To relay carrier and payload data to ground station

## Slide 22: EPS Overview (2 of 4)
Presenter: Name goes here
Component | Purpose
Servo motor | Used in releasing mechanisms and controlling the powered flight
Brushless motor | To maintain levelled flight
Buzzer | To help locate the carrier after landing

## Slide 23: EPS Overview (3 of 4)
Presenter: Name goes here
Container Overview
Arduino nano
Servo motors
3.3V regulator
XBee
Two 3.6V batteries in series
Two 3.7V batteries in series
ESC
Brushless motor
Sensors and buzzer

## Slide 24: EPS Overview (4 of 4)
Presenter: Name goes here
Two 3.6V batteries in series
Arduino nano
Sensors
Servo motors
3.3V regulator
XBee
Payload Overview

## Slide 25: Container Electrical Block Diagram 1 of 2
Presenter: Name goes here
Battery(7.2V)
3.3V regulator
IMU
(MPU9250+
BMP280)
Buzzer
Switch
(ON/OFF)
Motor
ESC
Battery(7.4V)
Arduino nano
GPS
XBee
Servo 1
Servo 2
Servo 3
7.4V
7.4V
7.2V
3.3V
3.3V
5V
7.2V
The power will be controlled via switch which will be placed in an easily accessible area.
The buzzer will be activated once the carrier lands

## Slide 26: Container Electrical Block Diagram 2 of 2
Presenter: Name goes here
Interface Diagram
Arduino Nano
Buzzer
GPS
XBee
IMU
(MPU9250+
BMP280)
Servo 1
Servo 2
Servo 3
ESC
UART
UART
I2C
Digital
PWM 1
PWM 2
PWM 3
PWM 4

## Slide 27: Container Power Trade & Selection 1/2
Presenter: Name goes here
Model | Type | Nominal Voltage (V) | Capacity (mAh) | Power Capacity (Wh) | Weight (g) | Cost ($)
Forte ER14250 | Lithium | 3.6 | 1200 | 4.32 | 10 | 7.29
Orange ISR 18650 | Li – ion | 3.7 | 2000 | 7.4 | 44 | 3.26
BR-2/3AGCT4A | Lithium | 6 | 2400 | 14.4 | 50 | 9.89
Selected : Forte ER14250
Rationale : Is lightweight and has sufficient power capacity
Two batteries will be attached in series to provide 7.2V and a total power capacity
of 8.64Wh. They will be mounted on a custom made battery holder.

## Slide 28: Container Power Trade & Selection 2/2
Presenter: Name goes here
Model | Type | Nominal Voltage (V) | Capacity (mAh) | Power Capacity (Wh) | Max. Continuous Discharge Current | Weight (g) | Cost ($)
PANASONIC NCR18650B | Li - ion | 3.7 | 3400 | 12.58 | 30A | 46 | 8.53
SONY VTC6 18650 | Li - ion | 3.7 | 3000 | 11.1 | 20A | 47 | 10.9
BR-2/3AGCT4A | Lithium | 6 | 2400 | 14.4 | 4A | 50 | 9.89
Selected : PANASONIC NCR18650B
Rationale : Greater power capacity and high discharge current
Two batteries will be attached in series to provide 7.4V and a total power capacity
of 25.16Wh to the motor. They will be placed in a battery holder.

## Slide 29: Container Power Budget 1 of 2
Presenter: Name goes here
Component | Current (mA) | Voltage (V) | Duty Cycle (%) | Power Consumption (Wh) | Source
Arduino nano | 19 | 5 | 100 | 0.19 | Datasheet
MPU9250 | 3.93 | 3.3 | 100 | 0.02593 | Datasheet
BMP280 | 1.12 | 3.3 | 100 | 0.00739 | Datasheet
GPS | 23 | 3.3 | 100 | 0.151 | Datasheet
XBee | 120 | 3.3 | 100 | 0.792 | Datasheet
Servo (tail) | 300 | 7.2 | 0.025 | 0.108 | Datasheet
Servo (x2) (deploying mechanism) | 300 | 7.2 | 0.00833 | 0.036 (x2=0.072) | Datasheet
Buzzer | 20 | 5 | 12.5 | 0.0125 | Datasheet

## Slide 30: Container Power Budget 2 of 2
Presenter: Name goes here
Component | Current (mA) | Voltage (V) | Duty Cycle (%) | Power Consumption (Wh) | Source
Voltage regulator | 5 | 7.2 | 100 | 0.072 | Datasheet
Motor | 30A | 7.4 | 0.025 | 11.1 | Datasheet
Total power consumption by circuit : 1.43Wh
Total power consumption by motor : 11.1Wh
Available total power capacity : 8.64Wh
Available total power capacity : 25.16Wh
Margin of Power consumption : 7.21Wh
83.44%
Margin of Power consumption : 14.06Wh
55.88%
Conclusion : Both combination of batteries have sufficient power to operate the carrier for 2hrs

## Slide 31: Payload Electrical Block Diagram 1 of 2
Presenter: Name goes here
Battery(7.2V)
Switch
(ON/OFF)
Arduino nano
3.3V regulator
XBee
BMP280
MPXV7002DP
7.2V
7.2V
7.2V
3.3V
5V
3.3V
The power will be controlled via switch which will be placed in an easily accessible area.
Two batteries are attached in series to provide 7.2V
Servo 1
Servo 2
7.2V

## Slide 32: Payload Electrical Block Diagram 2 of 2
Presenter: Name goes here
XBee
BMP280
MPXV7002DP
Interface Diagram
Arduino Nano
Servo 1
Servo 2
UART
I2C
Analog
PWM 1
PWM 2

## Slide 33: Payload Power Trade & Selection
Presenter: Name goes here
Model | Type | Nominal Voltage (V) | Capacity (mAh) | Power Capacity (Wh) | Weight (g) | Cost ($)
Forte ER14250 | Lithium | 3.6 | 1200 | 4.32 | 10 | 7.29
Orange ISR 18650 | Li – ion | 3.7 | 2000 | 7.4 | 44 | 3.26
BR-2/3AGCT4A | Lithium | 6 | 2400 | 14.4 | 50 | 9.89
Selected : Forte ER14250
Rationale : Is lightweight and has sufficient power capacity
Two batteries will be attached in series to provide 7.2V and a total power capacity
of 8.64Wh. They will be mounted on a custom made battery holder.

## Slide 34: Payload Power Budget 1 of 2
Presenter: Name goes here
Component | Current (mA) | Voltage (V) | Duty Cycle (%) | Power Consumption (Wh) | Source
Arduino nano | 19 | 5 | 100 | 0.19 | Datasheet
BMP280 | 1.12 | 3.3 | 100 | 0.00739 | Datasheet
XBee | 120 | 3.3 | 100 | 0.792 | Datasheet
MPXV7002DP | 10 | 5 | 100 | 0.108 | Datasheet
Servo (x2) (deploying mechanism) | 300 | 7.2 | 0.00833 | 0.036 (x2=0.072) | Datasheet
Voltage regulator | 5 | 7.2 | 100 | 0.072 | Datasheet

## Slide 35: Payload Power Budget 2 of 2
Presenter: Name goes here
Total power consumption by circuit : 1.241Wh
Available total power capacity : 8.64Wh
Margin of Power consumption : 7.399Wh
85.63%
Two batteries of 4.32Wh power capacity will be connected in series to give a total
of 8.64Wh power capacity.
Conclusion : Battery is sufficient to power all the components throughout the flight

## Slide 36: Flight Software (FSW) Design
Aniruddh Pandey

## Slide 37: FSW Overview 1 of 3
Presenter: Name goes here
Programming languages : C/C++
Development Environment : Arduino IDE
Carrier FSW Tasks:
Calibrate sensors and send the reference point for altitude to payload
Decide the software state based on altitude
Sample and process all data from sensors
Maintain telemetry with GCS
Command the release of payload
Act as a relay between payload and GCS
Keep updating EEPROM
Activate audio beacon on landing
Payload FSW Tasks:
Receive reference point from carrier for the altitude
Sample and process all data from sensors
Start telemetry when commanded by the carrier
Keep updating EEPROM

## Slide 38: FSW Overview 2 of 3
Presenter: Name goes here
Carrier FSW Architecture
Power ON
Initialize and Calibrate Sensors
Detect apogee and deploy wings
Start telemetry
Release the payload
Relay the payload data to GCS
Detect Landing
Stop all functions
Activate audio beacon
Start powered flight

## Slide 39: FSW Overview 3 of 3
Presenter: Name goes here
Payload FSW Architecture
Power ON
Receive calibration data from carrier
Receive command to start telemetry
Start telemetry
Release the heat shield
Deploy parachute
Detect Landing
Stop all functions
Detect 500m altitude

## Slide 40: Container FSW State Diagram 1 of 4
Presenter: Name goes here
Power ON
Initialize and set variables
Read EEPROM for software state
If
State=0
Set software state value
Calibrate sensor and send data to payload
Set software state to 1
Take sensor readings for altitude
If
Apogee detected
Set software state to 2
Update the state to EEPROM
Write all data to EEPROM
Update the state to EEPROM
Yes
Yes
No
No
Move on to respective stage

## Slide 41: Container FSW State Diagram 2 of 4
Presenter: Name goes here
Deploy wings
Start helical manoeuvre
Set software state to 3
Start telemetry at 1Hz
Increment packet count
Update all data into EEPROM
If
Altitude <=1510
Set software state to 4
Record the position at that moment
Stop powered flight
Continue the powered flight for 300m
Yes
No
Update the state to EEPROM
Stop helical
manoeuvre
Start powered flight
If 300m achieved
Write data to EEPROM
No
Yes

## Slide 42: Container FSW State Diagram 3 of 4
Presenter: Name goes here
Release the payload
Command payload to start telemetry
Set software state to 5
Receive payload telemetry
Relay it to GCS
Update all data into EEPROM
If
Altitude <5
Set software state to 6
Stop all functionalities
Yes
Update the state to EEPROM
Activate audio beacon
No
A timer based interrupt will be set at 1Hz for the telemetry

## Slide 43: Container FSW State Diagram 4 of 4
Presenter: Name goes here
FSW Recovery :
All the necessary data for smooth operation of flight software will be stored in the microcontroller’s EEPROM
Data stored in EEPROM :
Flight software state
Packet count
Sensor calibration data
Variables controlling sub-stages of flight
The position of carrier at the start of powered flight
The processor can reset due to software hang, overheating or if the power supply interrupts

## Slide 44: Payload FSW State Diagram 1 of 3
Presenter: Name goes here
Power ON
Initialize and set variables
Read EEPROM for software state
If
State=0
Set software state value
Receive calibration data
Set software state to 1
Wait for START command from carrier
If
“START”
Set software state to 2
Update the state to EEPROM
Write all data to EEPROM
Update the state to EEPROM
Yes
Yes
No
No
Move on to respective stage

## Slide 45: Payload FSW State Diagram 2 of 3
Presenter: Name goes here
Start telemetry at 1Hz
If altitude<=500m
Continue telemetry
Update all data to EEPROM
Yes
No
Release the heat shield
Deploy the parachute
If altitude<=5m
Stop all functionalities
Update the state to EEPROM
No
Yes
Increment packet count

## Slide 46: Payload FSW State Diagram 3 of 3
Presenter: Name goes here
FSW Recovery :
All the necessary data for smooth operation of flight software will be stored in the microcontroller’s EEPROM
Data stored in EEPROM :
Flight software state
Packet count
Sensor calibration data
The processor can reset due to software hang, overheating or if the power supply interrupts

## Slide 47: Software Development Plan
Presenter: Name goes here
Prototype and Prototyping environment :
All the sensors will be tested separately on breadboard
Arduino IDE will be used to develop the software and test it
The data stream will be checked on Arduino Serial Monitor
Test methodology :
All sensors will be tested via breadboard and the values will be monitored using the
Serial monitor of Arduino IDE
Release mechanisms of wings, payload and heat shield will be tested
Data recovery algorithm will be tested
Working of XBee will be tested by separating them at appropriate distances

## Slide 48: Ground Control System (GCS) Design
Aniruddh Pandey

## Slide 49: GCS Overview
Presenter: Name goes here
Science Payload Data
.csv files and graph
GCS XBee
GCS GUI
Payload XBee
Carrier XBee
Start telemetry command
Receive telemetry data
Receive telemetry data
Send calibration command
XBee USB Adapter
GCS Antenna
GCS GUI

## Slide 50: GCS Design
Presenter: Name goes here
Data from Carrier XBee
GCS Antenna
GCS XBee
XBee USB Adapter
GCS GUI
RP SMA
Male to Female
connector
The laptop can operate for at least 5 hours
A backup laptop will be present with GUI installed in it
The laptop will be kept under shade and a cooling fan will be used
Updates for OS, if any, will be done the beforehand and the auto update feature will be disabled
The laptop will be disconnected from internet on the day of launch

## Slide 51: GCS Antenna Trade & Selection
Presenter: Name goes here
Antenna | Gain (dBi) | Connector | VSWR | Frequency (GHz) | Polarization | Cost
Omni SMA Male Antenna | 5 | SMA | <2.0 | 2.4-2.5 | Vertical | 2.59
Magnetic Mount Antenna | 3 | SMA-Male | <2.0 | 2.4-2.483 | Linear | 2.04
Selected : Omni SMA Male Antenna
Rationale: Better gain
Radiation Pattern